## Slide 1: 2021-22 Project
Minimum requirements
Roger.espasa@upc.edu

## Slide 2: 1. Basic Instruction Set
You can use RISCV
Or alternatively use a custom
  Architectural state
    32 registers, each 32b (r0 through r31)
    Special register rm0, 32b, for holding the PC the OS should return to on exceptions
    Special register rm1, 32b, for holding an @ for certain exceptions
    [optional] Special register rm2, 32b, holding information on the type of exception
  Interface to OS
    Processor boots from address 0x1000
    Exceptions will always jump to address 0x2000
  Basic Instruction Set
    Each instruction is 32bits.
    ADD r1, r2  r3 // Add two registers
    SUB r1, r2  r3 // Subtract two registers
    MUL r1, r2r3 // Multiply two registers
    LDB 80(r1)  r0 // Load Byte; base register + offset
    LDW 80(r1)  r0 // Load Word; base register + offset
    STB r0  80(r1) // Store Byte; base register + offset
    STW r0  80(r1) // Store Word; base register + offset
    BEQ r1, offset // if r1==r2, PC=PC+offset
    JUMP r1, offset // PC = r1 + offset
The minimum instructions that need to work in your project are
  ADD, SUB, MUL, LDB, LDW, STB, STW, BEQ, JUMP (whatever ISA you decide to use)

## Slide 3: If you use a custom ISA… Suggested Encoding
opcode
31 25
dst
24 20
src1
19 15
src2
14 10
000000000
9 0
R-type instructions
M-type instructions
B-type instructions
opcode
31 25
dst
24 20
src1
19 15
offset
14 0
opcode
31 25
OffsetHi
24 20
src1
19 15
Src2
OffsetM
14 10
OffsetLo
9 0
R-type: ADD, SUB, MUL
M-type: LDB,LDW,STB,STW
B-type:
  BEQ: Offset[14:0] = {OffsetHi, OffsetLo}
  JUMP: Offset[19:0] = {OffsetHi, OffsetM, OffsetLo}
Optional instructions
  MOV rm0, dst: encoded as M-type, src1=0, offset=0
  TLBWRITE r0,r1: encoded as B-type: src1=r0, src2=r1, offsetLo=0 for ITLB, offsetLo=1 for DTLB
  IRET: encoded as B-type: src1=0, src2=0, offsethi=0, offsetlo=0
Instruction | Opcode
ADD | 0x0
SUB | 0x1
MUL | 0x2
LDB | 0x10
LDW | 0x11
STB | 0x12
STW | 0x13
MOV | 0x14
BEQ | 0x30
JUMP | 0x31
TLBWRITE | 0x32
IRET | 0x33

## Slide 4: 2. Caches
Instruction Cache
  4 cache lines, 128b per cache line
  You can pick any replacement policy you want
  You can pick any associativity you want
Data Cache
  4 cache lines, 128b per cache line
  You can pick any replacement policy you want
  You can pick any associativity you want
Memory
  5 cycles to go to memory
  5 cycles to return data from memory to processor
[optional] Support unaligned LDW, STW

## Slide 5: 3. PIPELINE BASICS
5 or more stage pipeline
Artificially make the MUL instruction take 5 execution stages.
  So the minimal pipeline for it would be:
    F, D, M1, M2, M3, M4, M5, WB
  You can add other stages to the above pipeline if you need it in your machine
Full set of bypasses
Store buffer of some sort
ROB or HF or FF

## Slide 6: 4. Adding Virtual Memory
Virtual memory architecture
  Virtual Address is 32bits
  Physical Address is 20bits
  Pages are 4KB
Translation Scheme
  Simply add some displacement to bits [31:12]
  For example: PA = VA + 0x8000;
Privilege Scheme
  We add another special register rm4
  Bit 0 in rm4 holds the current privilege of the machine
    0 for users
    1 for supervisor
The machine boots in supervisor mode
When in supervisor mode, virtual memory is disabled
  This will simplify your mini-os and your logic
  So don’t look up the TLB when rm4[0] = 1
Therefore:
  Processor boots from PHYSICAL address 0x1000
  Exceptions jump to PHYSICAL address 0x2000

## Slide 7: 4. Changes for Virtual Memory
Add an iTLB and a dTLB
On a TLB miss:
  Save the faulting PC to rm0
  Save faulting @ to rm1
  [optional] save additional info to rm2 that your mini-os may need
  Jump to physical address 0x2000
  Switch from user-mode to supervisor mode by flipping bit 0 of rm4
The Mini-OS code will do something like
  Store r5  [A]
  Store r6  [B]
  MOV rm1  r5
  ADD r5, #8000  r6 // r6 represents the translation of r5
  TLBWRITE r5, r6 // (r5 = virtual @, r6 = physical @)
  Load [A]  r5
  Load [B]  r6
  IRET
Notice we added 3 new instructions
  MOV from rm1 to r5
  TLBWrite r5, r6 = adds the pair <va,pa> to our tlb; faults if not privileged
  IRET = jumps to the @ in rm1 and lowers the PSW (rm4[0:0]) to user

## Slide 8: Virtual Mem for RISCV
If you want to follow riscv
Create the satp register
Ignore the SV39/SV48 model
Define a simple displacement model
  Put in satp the “displace” value
  Translation is va + satp[19:0]
You can do a hardware page Walker
  Instead of the “tlbwrite” instruction

## Slide 9: Performance Tests
Note: you of course have to have other functional tests beyong these 3 performance tests
Count how many cycles the three following tests take on your machine
Buffer_sum
  int a[128], sum = 0;
  for (i=0; i<128; i++) { sum += a[i]; }
Mem_copy
  int a[128], b[128];
  for (i=0; i<128; i++) { a[i] = 5; }
  for (i=0; i<128; i++) { b[i] = a[i]; }
Matrix multiply
  int a[128][128], b[128][128], c[128][128];
  for (i=0; i<128; i++) {
  for(j =0;j<128;j++) {
  c[i][j] = 0;
  for(k = 0; k <128; k++ ) {
  c[i][j] = c[i][j] + a[i][k] * b[k][j];
  }
  }
  }

## Slide 10: Bonus
Branch Predictor
DMA engine
Out-of-order

## Slide 11: Project Delivery: Jan 24 & 25th
1h per team, C6-E101
A Block diagram in pipeline form of your design
One page per instruction type explaining what the instruction does in each stage
  1 page for Load
  1 page for Store
  1 page for Branch/Jump
  1 page for Arithmetic
  1 page for Exceptions+ROB/HF/FF
One page with your performance results
Your RTL project (send by mail in tar file)
We’ll meet in my office/virtually for 30-45min and review your code and show me waveforms of your rtl

## Slide 12: Project Teams
Team |  |  |  | Delivery
1 | Arnau Cinca |  |  | 9am 24st
2 | Roger Garcia | Andreu Girones |  | 10am 24st
3 | Pablo Vizcaino |  |  | 11am 24st
4 | Joan Vinyals | Guillem Ramirez |  | 12am 24st
5 | Alejandro Alonso | Sergi Palomas | +1 | 1pm 24st
6 | Asier Fernandez |  |  | 9am 25th
7 | Javier Salamero | Xavier Carril |  | 10am 25th
8 | Nitish | Suraj |  | 11am 25th
9 | Eric Rufart |  |  | 12am 25th
10 | Yo |  |  | 1am 25th
11 | Nikolaos | Sergio Garcia |  | 9am 26th
12 | Luka | Matej |  | 10am 26th
12 | Alex |  |  | 11am 26th